# Wireless LAN PCI Card                        ZXP-122

Wireless LAN PCI Card
IEEE 802.11b, WEP Compliant

with external antenna and SMA-R connector

Features :

• Complies with the IEEE 802.11b 2.4GHz (DSSS) standard.

• High data transfer rate - up to 11Mbps.

• Supports 64/128-bit WEP Data Encryption function.

• Supports peer-to-peer communication among any wireless users, no Access Point  is required.

• Detachable antenna with magnetic base provides convenience to locate the antenna.

• Automatic fallback increases data security and reliability.

• Supports the most popular operating system: Windows 98SE/Me/NT/2000/XP and Linux.

Specification :

| Product | ZXP – 122 PCI |
| --- | --- |
| Standards | IEEE 802.11b |
| Bus Type | PCI V2.1 |
| Chipset | ADMtek |
| Frequency Band | 2.400~2.4835GHz (Industrial Scientific Medical Band) |
| Modulation | CCK@11/5.5Mbps, DQPSK@2Mbps, DBPSK@1Mbps |
| Radio Technology | Direct Sequence Spread Spectrum (DSSS) |
| Data Rate | 11/5.5/2/1Mbps auto fallback |
| Security | 64/128-bit WEP |
| Antenna | External detachable dipole antenna with magnetic base (Cable Length: 1M, Connector: SMA connector) |
| Drivers | Windows 98SE/Me/2000/XP and Linux |
| LEDs | 2 LEDs Power/Link |
| Power Voltage | 3.3V |
| Transmit Power | 16 dBm |
| Sensitivity | -80 dB (11 Mb) -84 dB (2Mb) |
| Dimension | 19(H) x 133(W) x 121(D) mm |
| Temperature | 32~131°F (0 ~55°C) |
| Humidity | 5-95% (Non condensing) |
| Certification | FCC , CE |
| Warranty | 12 months (24 months EU) |

### Distribution/Sales

i4 Portfolio Praha 					http://www.i4shop.net

Sarajevska 29						sales@i4shop.net

CZ-120 00 Praha 2

Czech Republic, EUROPE

phone: +420-222-560208

fax: +420-222-564295